BT-OG01A / BT-OG01B
TWI EEPROM Module for Odroid GO

Features: / - Designed for the Odroid GO expansion Port / - Usage of the 24LCXXA EEPROM Chips / - BT-OG01B Module Selection Pin / - Replaceable EEPROM Chip / - Integrated TWI pull up resistors / - 100 kHz communication frequency / - Status LEDs / Description: / The BT-OG01X is an EEPROM module designed for the expansion port of the Odroid GO to store data. It can be used with the official BT-GoAsm Software, but can also be used in custom programs. The BT-OG01B is embedded in the BT-OG02 EEPROM Array.		Pinout: / Pin descriptions: / YLED / NC -> For BT-OG01A this pin serves the Yellow LED, on the BT-OG01B this pin is not connected. / RLED / CSEL -> On the BT-OG01A this pin controlls the red LED, on BT-OG01B this pin serves as the chip selection pin, which toggles the TWI address to be 0x51 instead of 0x50. The red LED on the BT-OG01B shows the state of selection. / SDA -> TWI Data / SCL -> TWI Clock / VCC -> 3.3V

Blockdiagram: